## Slide 1: Lattice Boltzmann method
CDISE, PhD-2
Andrey Olhin

## Slide 2: Outline
CFD. Relevance and applicability
Advantages of Lattice Boltzmann method
Lattice Boltzmann method in nutshell.
  Discretization of equations. BGK model
  Discretization of domain
  Pros and Cons
What can we do with such a model?
Homework tips and algorithm

## Slide 3: What is Fluid Flow?

## Slide 4: What is Fluid Flow?
meteorological phenomena (rain, wind, hurricanes, floods, fires)
environmental hazards (air pollution, transport of contaminants)
heating, ventilation and air conditioning of buildings, cars etc.
combustion in automobile engines and other propulsion systems
interaction of various objects with the surrounding air/water
complex flows in furnaces, heat exchangers, chemical reactors etc.
processes in human body (blood flow, breathing, drinking . . . )
Fluid flows encountered in everyday life include:

## Slide 5: What is CFD?

## Slide 6: What is CFD?
mathematical modeling (partial differential equations)
numerical methods (discretization and solution techniques)
software tools (solvers, pre- and postprocessing utilities)
Computational Fluid Dynamics (CFD) - provides a qualitative (and sometimes even quantitative) prediction of fluid flows.
CFD enables scientists and engineers to perform ‘numerical experiments’ (i.e. computer simulations) in a ‘virtual flow laboratory’
Lattice Boltzmann method!

## Slide 7: What is CFD?

## Slide 8: Outline
CFD. Relevance and applicability
Advantages of Lattice Boltzmann method
Lattice Boltzmann method in nutshell.
  Discretization of equations. BGK model
  Discretization of domain
  Pros and Cons
What can we do with such a model?
Homework tips and algorithm

## Slide 9: Size matters
Meters
Micro-nanometers (10^(-6)-10^(-9))

## Slide 10: LBM’s place in the system
Notes: Mean free path

## Slide 11: Examples

## Slide 12: Outline
CFD. Relevance and applicability
Advantages of Lattice Boltzmann method
Lattice Boltzmann method in nutshell.
  Discretization of equations. BGK model
  Discretization of domain
  Pros and Cons
What can we do with such a model?
Homework tips and algorithm

## Slide 13: Lattice Boltzmann Method in nutshell
Mesoscopic
(Microscopic)
Macroscopic
Navier-Stocks eq.
Boltzmann eq.
Lattice Boltzmann
From the definition of VDF and its normalization:
Function is normalized to the mass of the gas in the system
Boltzmann eq.
!Only gases!
Navier-Stocks eq.

## Slide 14: Lattice Boltzmann Method in Nutshell
Let’s write down the Boltzmann equation:
and apply the Bhatnagar-Gross-Krook (BGK) approximation of collision integral (we decide that system is uniformly equilibrated):
Hence, the equation transforms to:
Where is equilibrium Maxwell-Boltzmann distribution function. Also, equilibrated system is connected to the macroscopic values as:

## Slide 15: Discretization of domain
Lattice Boltzmann is the method of numerical modeling of fluid dynamics. So, numerical modeling involves performing the following steps:
Discretization of the domain.
Discretization of equations.
So, first let’s imply the simples 1D grid for example:
The distance between nodes of grid is:
It is also called gridstep.
The time that passes between iterations is:
It is timestep.
The value of timestep and grid step are represented
In Lattice Units.
We will omit the procedure of discretization from physical units to lattice units in this course

## Slide 16: Discretization of equations. BGK model
Let’s take a closer look on Boltzmann equation from previous slides:
We do next assumptions for simplicity:
Speed of propagation of perturbation between nodes: .
No external forces.
Also, it’s required to fluid parameters (density, mass flux) be determined in grid nodes.
As a result, we obtain:
The subscript related to the one of the discrete set of velocities .

## Slide 17: Discretization of equations. BGK model
The subscript related to the one of the discrete set of velocities .

## Slide 18: Discretization of equations. BGK model
The subscript related to the one of the discrete set of velocities .
Problem: How to discretize
– universal gas constant, – temperature, – dimensions, - velocity vector, - macroscopic velocity of gas.
!! It is for the vector we want to find the probability density!!
We already assumed that the molar mass is equal 1 (it doesn’t matter, only macroscopy density does).
What means ? It is transition to the local frame of reference.
Velocity is normalized to the local macroscopic velocity.

## Slide 19: Discretization of equations. BGK model
The subscript related to the one of the discrete set of velocities .
Problem: How to discretize
If assume that , try to compute and summarize after that by number of direction – it will not be agreement!

## Slide 20
There is an approach in of approximation of smooth functions in numerical modeling – expansion in Terms of Taylor series.
But it still will be not enough to converge to macroscopic variables. It also needed to compute “weight” coefficients.
*Xiaoyi He and Li-Shi Luo (1997) Phys. Rev. E 56, 6811
https://journals.aps.org/pre/abstract/10.1103/PhysRevE.56.6811
D2Q9
D3Q19
  Discretization of equations. BGK model

## Slide 21: Discretization of equations. BGK model
Remark: R and T are not in SI.
*Xiaoyi He and Li-Shi Luo (1997) Phys. Rev. E 56, 6811
https://journals.aps.org/pre/abstract/10.1103/PhysRevE.56.6811
D2Q9
D3Q19
- «speed of sound» in system
Speed of propagation of perturbations between nodes: .
Speed of propagation = speed of sound
Speed of sound: .
Limitation on the choice of parameters:

## Slide 22: Discretization of equations. BGK model
Streaming step
Collision step
The subscript related to the one of the discrete set of velocities .
Problem: How to discretize When calculate equilibrium distribution?
For completing the computation scheme its more relevant to use node.
Then, equation above may be divided into two components:
And last, but not least – Relaxation time.
– kinematic viscosity of fluid

## Slide 23: Lattice Boltzmann Method in Nutshell
For discretization of velocities directions mass and macroscopic velocity in every node will be equal to:

## Slide 24: LBM Initialization and simulation
Initialization:
Computation loop:
Compute the fluid density and velocity
Compute the equilibrium populations
Apply collision to find post-collision populations
Stream populations at boundaries according to the local boundary conditions.
Stream populations.
Increment the time step and go back to step 1.

## Slide 25: Boundary conditions in LBM
There are a great many variations of boundary conditions for Lattice Boltzmann method. I’ll show the simplest and most popular of them.
It is called “bounce-back” boundary condition. The physical meaning of this BC – no-slip for velocity.

## Slide 26: Outline
CFD. Relevance and applicability
Advantages of Lattice Boltzmann method
Lattice Boltzmann method in nutshell.
  Discretization of equations. BGK model
  Discretization of domain
  Pros and Cons
What can we do with such a model?
Homework tips and algorithm

## Slide 27: Lattice Boltzmann Method pros and cons
Pros:
Simplicity and scalability
The computations are local, its easy to parallel
The LBM is well suited to simulating mass-conserving flows in complex geometries such as porous media
Moving boundaries that conserve mass can be implemented particularly well in the LBM making it an attractive method for soft matter simulations.
Wide range of multiphase and multicomponent methods available for the LBM.
Cons:
LBM is memory-intensive
Is not particularly efficient for simulating steady flows
Non-compressible flows
The LBM is not appropriate for directly simulating long-range propagation of sound at realistic viscosities

## Slide 28: LBM Packages
Open source software:
Palabos
Open LB
WalLBerla
Ludwig
Commercial packages:
Dassault systems PowerFlow
ANSYS Discovery

## Slide 29: Outline
CFD. Relevance and applicability
Advantages of Lattice Boltzmann method
Lattice Boltzmann method in nutshell.
  Discretization of equations. BGK model
  Discretization of domain
  Pros and Cons
What can we do with such a model?
Homework tips and algorithm

## Slide 30: Permeability of rock samples
Definition | Parameter | Colour
Inlet |  | 
Outlet |  | 
Symmetry |  | 
Bounce-Back | Fig. 6 | 
Definition | Parameter | Colour
Inlet |  | 
Outlet |  | 
Symmetry |  | 
Bounce-Back | Fig. 6 | 
Porous media sample geometry with painted BCs
Bounce-Back BC scheme

## Slide 31
Up - Calculated pressure distribution averaged on the plane for three values of water content
Down – Dimensionless Permeability dependencies
Permeability of rock samples

## Slide 32: Overflow of different shapes

## Slide 33: Multiphase flows

## Slide 34: Outline
CFD. Relevance and applicability
Advantages of Lattice Boltzmann method
Lattice Boltzmann method in nutshell.
  Discretization of equations. BGK model
  Discretization of domain
  Pros and Cons
What can we do with such a model?
Homework tips and algorithm

## Slide 35
Homework tips
Sign | Description | Value
 | Length of tube, equivalent to L | 100
 | Diameter of tube, equivalent to 2*b | 20
 | Inlet pressure in LBM units. | 1.5
 | Outlet pressure in LBM units | 0.5
 | Relaxation time | ???
 | Number of time steps | ???
Sign | Description | Value
 | Length of tube, equivalent to L | 100
 | Diameter of tube, equivalent to 2*b | 20
 | Inlet pressure in LBM units. | 1.5
 | Outlet pressure in LBM units | 0.5
 | Relaxation time | ???
 | Number of time steps | ???

## Slide 36
Homework tips
Poiseuille velocity profile:
Streaming step
Collision step
!Play with relaxation time!

## Slide 37
Homework algorithm
*Initialize the domain* #(Q x Nx x Ny matrix)
*Initialize macroscopic fields*
*Initialize equilibrium at all nodes regarding to macroscopic field variables*
For timestep in simulation time:
*stream from boundary nodes* #counter clockwise starting from left boundary
*stream from corner nodes* #counter clockwise starting from top left corner
*stream on free nodes*
*collision on all nodes*
*Compute macroscopic variables by summation over the Q*
*Finish*

## Slide 38: Thank You for attention!
Email: Andrey.Olhin@skoltech.ru
Telegram: @AndreyOlhin